## Slide 1: CRANFIELD UNIVERSITY Applied Mathematics and Computing Group (AMAC) Multi-stepping procedure ICECREMO
Patrick Verdin & Chris Thompson
Bristol, 27 February 2006

## Slide 2: Review Multi-stepping ICECREMO 1
    Procedure successfully implemented
    Fully automated
    UNIX operating system
    Language: FORTRAN77
    Criterion for Restart based on Time

## Slide 3
End
Geometry
Update
yes
no
ALGORITHM ICECREMO1
Start
Define Substrate
Create Mesh (GAMBIT)
Int. FLUENT/ICECREMO1
Restart File
Solve Flow (FLUENT)
Predict Ice (ICECREMO1)
Multi-step

## Slide 4: Limitations Multi-Stepping Procedure ICECREMO 1
    Slow process (mesh, flow, interface Fluent/Icecremo)
    Difficulties to set-up droplets starting point
    Problems with the particle tracking routine (SPLAT)
    Difficulties with the automatic re-meshing in GAMBIT
    No update of the water height between steps
    No update of the surface temperature

## Slide 5
NACA 0012 – Ts = -26 C – Texp = 6min

## Slide 6
NACA 0012 – Ts = - 5.6 C – Texp = 6 min – 3 steps

## Slide 7: Conclusion Multi-stepping ICECREMO 1
    Results encouraging
    Validation report written
    Problems identified and addressed in unstructured version:
        Improve meshing and re-meshing
        Update water and ice heights, surface temperature between the steps
        Define criterion trigger new flow calculation
        Speed-up multi-stepping procedure

## Slide 8: Review Multi-stepping ICECREMO 2
    Two procedures successfully implemented
      Restart with flow update
      Restart without flow update (internal process)
    Fully automated
    Linux operating system
    Languages: C++ / Fortran
    3 criteria for Restart based on:
      Time (time-step defined by user)
      Ice height (ice height max defined by user)
      Automatic (determined automatically and based
      on chord length or cylinder diameter)

## Slide 9
Start
Define Substrate
Create Mesh (GAMBIT)
Predict Ice (ICECREMO2)
End
Geometry
Update
yes
no
Multi-Step
Temperature Update
Restart File
Solve Flow (FLUENT)
Water height Update
ALGORITHM ICECREMO2
Internal Multi-stepping (same Flow)
Multi-stepping with Flow Update

## Slide 10
CASE O5 - NATO/RTO – Ts=270.2K – Texp=330 s
Time crit: 20 steps
Ice crit: 10 steps
Auto crit: 20 steps

## Slide 11
CASE O6 - NATO/RTO – Ts=270.6K Texp=330s
Time crit: 20 steps
Ice crit: 10 steps
Auto crit: 17 steps

## Slide 12
NACA 0012 - NATO/RTO - C17 – Ts= -7 C – Texp=20min
Ice crit: 4 steps
Auto crit:10 steps

## Slide 13
NACA0012 – Ts = -26 C – Texp = 6min
Time crit: 3 steps
Ice crit: 20 steps
Auto crit: 6 steps

## Slide 14: Limitations Multi-Stepping Procedure ICECREMO 2
    Current procedure limited to cylinders and airfoils studies
    Loss of precision due to the interpolation Faces/Nodes for multi-stepping with Flow update
    Solving grid has to be structured (rectangles) due to Gambit’s limitations
    Procedure only adapted to CFD suite FLUENT

## Slide 15: Conclusion Multi-stepping ICECREMO 2
Implementation successful
Fully automated
Problems from structured version fixed:
  Improved automated process
  Updates of water and ice heights
  Update of surface temperature
  3 Criteria trigger new flow calculation
      Automatic criterion appeared to produce the most accurate results
  Good validation results
  Software delivered August 2005
  User-Guide written

## Slide 16: Potential Future Work Multi-stepping ICECREMO 2
    Coupling with de-icing procedure
    Coupling with adaptive mesh refinement
    Adapt to other geometries
    Adapt to other CFD packages
    Speed-up the whole procedure using parallel calculations